Performance Recommendations Cheat Sheet:
 KEEP EXPLAINATIONS HIGH LEVEL
GOLDEN RULES
1. Understand the target architecture
  1. Documents, bear in mind the effects of and on CPU Processing power, memory bandwidth, thermal load
2. Profile the application
  1. Don’t waste effort. Tools. Bottlenecks: CPU, bandwidth, synchronisation, shaders, texture upload[?], geometry
3. Avoid alpha blending
  1. When alpha blending is enabled, HSR isn’t run for those fragments and depth feedback is required. Depth tested but no depth write (can be occluded but cannot occlude). Submitting alpha blended draws after opaque ones allows the alpha blended primitives to be obscured and thus less fragments be processed for them. Implemented with shader patching.
4. Do not use discard
  1. Same issue as with alpha blending. opaque > alpha tested > blended
5. Perform clear
  1. Saves bandwidth (and power) by preventing colour buffer being loaded at the start of the frame. Also please invalidate framebuffers.
6. Use texture compression
  1. Reduces both memory footprint and bandwidth costs of your texture assets.
7. Use mip-mapping
  1. Increase texture cache efficiency, which reduces bandwidth and increases performance.
8. Do not update buffers mid-frame
  1. This causes stalls (slower frame time, wait for vertex processing to finish) and ghosting (increases memory allocation).
9. Do not force unnecessary synchronisation
  1. Stalls the graphics pipeline.
10. Move calculations up the pipe
  1. Fragment, vertex, CPU, pre-baked. Reduce the number of times calculations have to be performed.
- Group by material – Minimise the number of state changes and API calls to reduce CPU overhead. Note that batching is easier now that you don’t have to worry about depth order submission! Use texture atlases or arrays to apply per object. Also batch by update frequency (separate VBOs).
- Use indexed lists – less memory and less vertices to process
- Split CPU work into multiple threads – (ai, physics etc) to ensure the CPU doesn’t become a bottleneck.
- Use lower precision – double the fp arithmetic throughput.
- LoD – mipmapping, geometry (low poly models, bump maps, reflection passes, tessellation)
- Don’t use a depth pre-pass – no benefit because of HSR.
- Use on-chip memory for deferred rendering – save loads of bandwidth.
- Use Vulkan – explicit API allows PVR drivers to optimize more effectively (more information available). Designed for CPU multi-threading, reduced API overhead, and TBR passes (TODO elaborate).
GEOMETRY
- Geometric complexity – reducing the number of vertices results in faster frames. Less tiler work, less PB reads/writes/processing.
- Primitive type – for a mesh with static attributes: indexed triangles (better cache hit rate because of shared vertices), interleaved attributes, no unused attributes. Use meshOptimizer library
- Data type – FP16 > FP32 > INT (costs cycles to use FP math)
- Interleaving attributes – better cache efficiency
- Use VBOs in GLES – don’t waste time copying. Driver allocates multiple VBOs when dynamic to process multiple frames at once.
- Large draw call size – make the API overhead worth the work to be done in GLES.
- Avoid small screen-space triangles – avoid overloading rasterization and use small parameter buffer
- Face culling – reduces the number of polygons to be binned by the TA and rasterized by the ISP. It is important for workloads with many hundreds of thousands of polygons.
- Sorting geometry – don’t waste time sorting opaque by distance, you have to for blended geometry (furthest first), may be beneficial for alpha testing (closest first to occlude?). Sort by render state (materials, shaders, render target etc.) as resource switching is very expensive.
TEXTURES
- Texture size – aim for a 1 texel to pixel mapping to increase cache efficiency (reduce bandwidth). Try lossy compression before downsizing. Use POT textures for optimal hardware/driver performance.
- Compression – TODO promote PVRTC?
- Mipmapping – increase cache efficiency and prevents under-sampling aliasing.
- Sampling – use the fastest possible filtering: nearest > bilinear > cubic > trilinear > anisotropic. Avoid dependant texture reads (e.g. uv calculated in the shader) but can be hidden with lots of calculations. A texture read is no more than 32 bits.
SHADERS
- PVRShaderEditor – allowing you to see the exact PVR instructions.
- GLSL optimizer – core generic optimizations, not hardware specific, verify optimisations with PVRShaderEditor.
- Choose the right algorithm! – don’t waste time micro-optimising a bad algorithm. Mobile graphics hardware is not designed to handle some of the greatest techniques for desktop or console, as such a reduction in complexity is required for these techniques.
- Analyse your space transformations – don’t perform unnecessary space transformations? TODO I don’t get this at all lol
- Flow control – PowerVR offers full support for shader flow control without enabling an extension. Make use of dynamic branching to skip operations when the condition is met in the majority of cases.
- Shader group vote – use GL_EXT_shader_group_vote or VK_EXT_shader_subgroup_vote to ensure that all shaders in a [TODO tile?] take the same branch path.
- Precision – lowp > mediump > highp try best performance option first (good enough paradigm e.g. sampler technique). Use highp (32fp) for position calculations, bone matrices and complex scalar functions (sin, pow, log). Mediump and lowp are both fp16 on rogue, uses dedicated FP16 SOP ALU pipeline to perform two operations in parallel in one cycle!
- Swizzling – very cheap operation thanks to Rogue’s scalar architecture.
- Use varyings instead of per-fragment calculations wherever possible, bearing in mind: each varying requires additional space in the parameter buffer, and additional processing time for interpolation, and they are stored in on-chip memory thus increasing register pressure (potentially reducing occupancy), pack multiple varyings together has no performance penalty on Rogue.
- Use sampler precision appropriate to what you are sampling
- Uniforms – bear in mind that some uniforms may be stored in on-chip registers but large uniform arrays will be stored in system memory and accesses will thus cost bandwidth. Remove redundant uniform updates in between draw calls.
- Conversion costs – bear in mind that type conversions take ALU cycles.
- Don’t accidently vectorise calculations.
- PVR drivers take advantage of the const keyword.
SPECIFIC TECHNIQUES
- Multiple render targets – use on-chip memory (PLS or subpassInput) to reduce bandwidth. Don’t exceed 128b per pixel to prevent per-tile render target data spilling into system memory.
- Lighting – forward for small number of lights, deferred otherwise, fast thanks to on-chip memory. Compute based techniques like tiled deferred and forward+ require memory write out.
- Shadows – stencil shadow volumes is the fastest because of hardware stencil handling and on-chip buffers (solid shadows only). Shadow mapping requires results to be written to off-chip memory.
- MSAA – will require reduced tile size to store samples, but x2 is free!
- FXAA > CMAA > MLAA > SMAA – requires full screen pass. TODO can we use on-chip mem?
- SSAO – involves a lot of random access to the depth buffer -> use hierarchical depth buffer. Reduces the number of steps for ray intersection and improves cache efficiency (sampling small area).
- Any ray-marching technique – e.g. screen space reflections, half resolution buffer using PVR downsampling extension combined with hierarchical z buffer. Also try a local cube map.
- Separable kernels – gaussian blur, bloom, motion blur, depth of field – either multi-pass algorithm (e.g. horizontal and vertical) which uses lots of bandwidth, or single-pass which could be better or worse because more samples are required. (check out Epic’s full screen blur single pass technique)
- Sprite rendering – transfer overdraw to geometry, powervr has excellent vertex processing hardware
- Physically based rendering – environment map mip level based on sampled roughness value. Use branching instead of a variable LOD parameter to reduce the number of texture fetches!
- Tessellation/geometry shaders – may not be supported. Introducing new geometry reduces performance, using geometry shaders to cull geometry may result in a performance boost (check with PVRTune).
GLES
VULKAN

QUESTIONS: (things I’ve had to guess/need confirmation on)
- What are the advantages of using indexed geometry? VB + IB = less memory transferred to the GPU?
- Indexing reduces the overall amount of data sent to the GPU also?
Is discard alpha testing?
How is PowerVR is optimised for indexed triangle lists?
- Should I use a depth pre-pass if using alpha blending?
- Lighting methods? Shadow methods?
- TODO mention algorithm
- Does MaliTC work well on PVR and vice versa?
- Is there a difference in performance impact between alpha blending and discard?
- Are forward and deferred the same with no overdraw?
- Why favour alpha blending over discard? PR 4.4.1
- What is meant by tessellation and geometry hardware acceleration? Do they have their own data-masters? (see furian architecture guide)